## Slide 1
hardware support for OS
Instructor: William Zheng
Email: william.zheng@digipen.edu
PHONE EXT: 1745
Notes: 1

## Slide 2: Goals for this lecture
HW and SW
CPU - I/O Communication
  Interrupt handling
  DMA
  More details in chapter 13.1-13.2 of textbook
CPU modes
  Backward-compatibility modes
  Privilege modes

## Slide 3: HW & SW
Difference?
Important to know the distinction
  OS (SW)
  But what OS can do
    Limited by the hardware it’s running on

## Slide 4: Computer System Components

## Slide 5: Motherboard

## Slide 6: Chipset Block Diagram

## Slide 7: Device Control Registers
Status register
  Done bit
  Error bit
Data register
  Data to be printed
Control registers
  Commands
Status
Data IN
Data OUT
Control
Device Controller

## Slide 8: CPU – I/O Communication
From CPU to I/O
  Special instructions
  Memory-mapped I/O
    Device data and command registers mapped to processor address space
    Especially for large address spaces (graphics)
From I/O to CPU
  Polling
  Interrupt

## Slide 9: Special I/O Instructions
Instruction specially for I/O
  I/O ports
    Different address spaces for memory and I/O devices
  E.g. Intel IN, OUT instructions
    Register I/O instructions: IN/OUT move data between I/O parts and the EAX (32-bit I/O), AX (16-bit I/O) or AL (8-bit I/O) general registers.
    Block I/O instructions: INS/OUTS move blocks of data between I/O ports and memory space

## Slide 10: Memory-mapped I/O - I
Use memory read/write
  E.g. intel MOV instructions
  Specific addresses mapped to I/O devices
Status
Data IN
Data OUT
Control
Device Controller
Memory Address Space

## Slide 11: Memory-mapped I/O - II
Using software to wait for I/O
Can check status register at fixed times
Pros
  Fast response time (for program waiting)
Cons
  Low CPU utilization
//wait for I/O to be done
//done bit is on status register
while (done_bit==0) ;
//process further data for I/O

## Slide 12: HW Setup for Interrupt Handling
While waiting for I/O, do other jobs first
Wait for I/O device to assert interrupt signal
IF and IV register
  Interrupt flag
  Interrupt vector
    A number indicating I/O controller type
Instr. Reg
PC
Reg
CPU
Instruction decoder
ALU
IF
IV
Interrupt signal
1 interrupt
0 No interrupt
from I/O
Interrupt vector:
A number indicating I/O Controller Type.

## Slide 13: Interrupt Handling
Instr. Reg
PC
Reg
CPU
Instruction decoder
ALU
IF
IV
Interrupt line
Status
Data IN
Data OUT
Control
Device Controller
I/O device
performs
operation
Error or I/O complete
CPU transfer controls to
Interrupt
Handler (ISR)
ISR runs and returns
Set IF to 1
CPU executes other instructions
Fetch
Decode
Execute
Writeback
Check IF Flag and priority
IF = 0
IF = 1
CPU resumes running interrupted program
CPU initiates I/O operation

## Slide 14: Interrupt-Driven I/O Cycle

## Slide 15: Interrupts (Cont.)
3 kinds of interrupt
  Exceptions/Faults: Errors: e.g., divide by zero
  Hardware Interrupt: I/O!
  Software-generated interrupt: System calls
Maskable and non-maskable
  Maskable means turned-off
  Usually exceptions/faults are not maskable.
Interrupt priority
  Interrupt handling can be interrupted by higher priority interrupts.

## Slide 16: Interrupt Vector Table
Interrupt Vector
  Unique for each interrupt
ISR
  SW handling of interrupts
Interrupt Vector Table
  Intel – IDT
    Real addressing mode: IVT
    Protected mode: IDT
  Array of function pointers

## Slide 17: Intel Pentium Processor Event-Vector Table

## Slide 18: Interrupts (Cont.)
Interrupt mechanism also used for exceptions
  Terminate process, crash system due to hardware error
Page fault executes when memory access error
System call executes via trap to trigger kernel to execute request
Multi-CPU systems can process interrupts concurrently
  If operating system designed to handle it
Used for time-sensitive processing, frequent, must be fast

## Slide 19: How does CPU transfer control to ISR?
Must know the address of a function to call a function.
Where is the interrupt vector table located?
  Memory
We want to know address containing the starting address of ISR for vector N
  Base Address + 8 * N for 64 bit
  Base Address + 4 * N for 32 bit
Question: how does the HW know where is the base?
Hardcoded (0x0000 to 0x03ff) during real mode
IDTR (Interrupt Descriptor Table Register) (Protected mode)
  Who sets up the IDTR?
  Who sets up the IDT?
Memory
.
.
.
0
1
.
.
.
2
N
.
.
.
N-1
ISR ADDRESS
0x…
0x…
0x…
0x…
0x…

## Slide 20: DMA: Motivation Scenario
Copy 1KB from Disk 1 to Memory (Disk Read)
A simple way:
  CPU req Disk1 controller for 1st byte
  Disk1 prepares the byte. Put it in Data-IN register.
  Interrupt CPU
  ISR reads the byte in Data-IN
Status
Data IN
Data OUT
Control
Disk1 Controller
Status
Data IN
Data OUT
Control
Other Device Controller
Memory
CPU

## Slide 21: DMA Scenario (Fig 13.5 Textbook)

## Slide 22: DMA Transfer Operation

## Slide 23: Direct Memory Access - I
Allow devices to read/write memory directly without CPU intervention
Does not mean accessing the memory in the same cycle
  Whether multiple devices (e.g. CPU) can access the memory at the same time depends on the memory design
Allows CPU processing to be in parallel with device to memory communication
  Reduce number of interrupts

## Slide 24: Direct Memory Access - II
Used to avoid programmed I/O (one byte at a time) for large data movement
Requires DMA controller
Bypasses CPU to transfer data directly between I/O device and memory
OS writes DMA command block into memory
  Source and destination addresses
  Read or write mode
  Count of bytes
  Writes location of command block to DMA controller
  Bus mastering of DMA controller – grabs bus from CPU
    Cycle stealing from CPU but still much more efficient
  When done, interrupts to signal completion
Version that is aware of virtual addresses can be even more efficient – DVMA (allows a device to perform a transfer from two memory-mapped devices without the intervention of the CPU or the use of main memory as a staging ground)

## Slide 25: Access HW device
User program access device directly?
  User program talks with device driver via system calls open(), read(), write() etc
  Protect data from access-control violations
  Erroneous use leads to crash

## Slide 26: How does this code execute?
int main()
{
  int add;
  int *add_p;
  scanf(“%d”, &add);
  add_p = (int*) add;
  *add_p = 0;
}
libc functions : read() and write()
Context switch from user level
to kernel mode

## Slide 27: MS-DOS and Intel 8088
Text/Code
Data
OS
*add_p = 0;
What happens?

## Slide 28: CPU privilege modes
Kernel (Supervisor mode) and user mode
Privileged instructions
  e.g. change the idtr value
Other instructions
  e.g. add, sub etc
Instruction Set
Privileged Instructions
Other Instructions
Set of instructions supported by the CPU